Farming-Microcontrol Labs –IITG 2015/2016

Farmingdale state college

Electrical Engineering Technology and Computer Engineering Technology Department
www.farmingddale.edu

IITG 2015-2016 Farming-Microcontroller

Use software simulation to foster student learning in microcontroller related LABs and projects
Supported by IITG 2015-2016

By

Prof. Marjaneh Issapour

Prof. Lijian Xu

( SUNY, USA

Project Abstract

### Microcontrollers are widely used in homes, offices, cars, factories, etc., and they have been an essential component of electrical and computer engineering education. Microcontrollers and their applications normally involve both software and hardware. It means that in microcontroller related LABs and projects, students often need to test and troubleshoot the software they develop on hardware platforms they build. This is often a challenging task for students because of the nature of software/hardware co-design. In this project, we aim at using software simulation to improve students' learning experience in microcontroller LABs and projects. Specifically, we have the following objectives: i) to help the students complete their microcontroller related LABs and projects in a more manageable way; ii) to design simulation demos that can be used in lectures to help the students understand the course materials; and iii) to reach out to high school students with microcontroller simulations in order to promote their interests in studying STEM in college.

Project Progress

## 1. Spring 2016: We will purchase the Proteus VSM software, install it on our LAB computers, and get familiar with it. (Proposal)

Proteus VSM software was purchased  and installed on our LAB computers at the end of Spring 2016. We started to work on the step 2 from June 2016.

## 2. Summer 2016: the PI and co-PI will develop the LABs and demos using Proteus VSM software (Proposal)

We have developed 4 labs and demos to enhanced students learning experiences of Microcontrollers and Microprocessors.

Lab1   Introduction to Software Tool of Proteus

Objectives
1. To be familiar with software tool of Proteus and MPLAB.

2. To understand how to make a project using MPLAB and then get the hex file of the software of the project.

3. How to simulate the hex file using Proteus.

Introduction

MPLAB and Proteus are the backbones of the microprocessor and microcontroller based systems, since using MPLAB we can build the software of the project using Assembly language, and then we can simulate the project virtually using Proteus, finally we can download the program on the microcontroller and see the result on hardware board.

Assignment

1. write a program in assembly language format to perform turning LED on.

2. Simulate hex file in Proteus 8.

Procedures

p1. Create a project named Lab_demo_1_intro in MPLAB:

FIG 1

demo_1_intro. asm

;************************************************************************

; Filename: IITG Demo 1 Introduction for EET 418L

; Function:	turn on LED.

;

; Author: Marjaneh Ispour and Lijian Xu

; Date: July 8, 2016

;************************************************************************

#include <GENERAL.h>

; ================	EQUATES  =========================================

; File register EQUATES

; =======================================================================

__CONFIG	0X3FF2		;This is the control bits for CONFIG register

ORG			0X0000		;RESET or WDT reset vector

GOTO		START

ORG			0X0004		;Regular INT vector RESERVE THIS SPACE.  DON'T USE IT

RETFIE

START	;First prepare PORTA and PORTB

BSF			STATUS,RP0	;switch to bank 1

MOVLW 		0x00

MOVWF		TRISB    	;set all PORTB bins as output

BCF			STATUS,RP0	;switch back to bank0

MOVLW		0x80		; RB7 is on

MOVWF		PORTB		;

GOTO		$

END						; assembler directive, not an instruction

p2. run simulation in Proteus 8.

FIG 2.

Important: R1 is 470 ohms.

Lab2   Blink LED

Objectives
1. To get familiar with programming and using PIC16F84 microcontroller.

2. To know how to make a delay loop with certain value.

3. To realize how PIC16F84A microcontroller deals with timing issues.

4. To know how to simulate these delay functions using Proteus

Procedures

p1. create MPLAB project named: demo_2_blink_LED

FIG 3.

The project includes following demo_2_blink_LED.asm

;************************************************************************

; Filename: IITG_demo_2_blink_LED

; Function:	use three DIP switches to control 8 LEDs.

; ;

; Author: Professor Ispour and Professor Xu

; Date: July 12, 2016

;************************************************************************

#include <GENERAL.h>

; ================	EQUATES  =========================================

; File register EQUATES

TEMP1		EQU		0x0C ; picks a file register for TEMP

TEMP2		EQU		0x0D ; picks a file register for TEMP2

TEMP3		EQU		0x0E ; picks a file register for TEMP2

TEMP		EQU		0x0F

; =======================================================================

__CONFIG	0X3FF2		;This is the control bits for CONFIG register

ORG			0X0000		;RESET or WDT reset vector

GOTO		START

ORG			0X0004		;Regular INT vector RESERVE THIS SPACE.  DON'T USE IT

RETFIE

MOVLF	MACRO		DEST,LIT	;Macro for moving a literal to a file register

MOVLW		LIT

MOVWF		DEST

ENDM

MOVFF	MACRO		SRC,DEST	;Macro for moving a content of File Register 1 to a file register 2

MOVF		SRC,W

MOVWF		DEST

ENDM

SUBFF	MACRO		Reg1,Reg2	;Macro for File Reg1 - File Reg 2

MOVF		Reg2		;Move Reg2 to W

SUBWF		Reg1,W		;Reg1 - Reg2, save to W

ENDM

THREE_LOOP_DELAY

MOVLF      TEMP1, 0X2

LOOP1	MOVLF      TEMP2, 0X25

LOOP2   MOVLF      TEMP3, 0X255

LOOP3

DECF TEMP3, F

BTFSS STATUS,Z

GOTO LOOP3

DECF TEMP2, F

BTFSS STATUS,Z

GOTO LOOP2

DECF TEMP1

BTFSS STATUS, Z

GOTO LOOP1

RETURN

START	;First prepare PORTA and PORTB

BSF			STATUS,RP0	;switch to bank 1

MOVLF		TRISB,0x07	;Upper five bits are output PINs, lower three are input pins

BCF			STATUS,RP0	;switch back to bank0

LOOP

CLRF		TEMP		; clear TEMPB for PORTB

;Now we scan the input pins and turn on/off LEDs accordingly

MOVLW		0x80		;

MOVWF		TEMP		; update TEMPB

IORWF		TEMP,F		; update TEMPB

MOVFF		TEMP,PORTB	; udpate PORTB

call 		THREE_LOOP_DELAY

MOVLW		0x00		;

MOVWF		TEMP		; update TEMPB

IORWF		TEMP,F		; update TEMPB

MOVFF		TEMP,PORTB	; udpate PORTB

call 		THREE_LOOP_DELAY

GOTO		LOOP		; repeat

GOTO		$

END						; assembler directive, not an instruction

p2. simulate hex file at Proteus:

FIG 4.

Important: delay time can be adjust at three_loop_delay.

Lab3   LED Display

Objectives
1. To get know how to design some logic functions using microcontroller PIC16F84A.

2. To get familiar with interfacing LED display to PIC16F84A and make a flasher.

Procedures

p1. create a project in MPLAB named: demo_3_display_LED.

FIG 5.

demo_3_display_LED.asp

;************************************************************************

; Filename: IITG Demo 3 Display LEDs													*

; Function: A program that demonstrates I/O procedures by lighting      *

; different LED configurations based on the position of switches        *

; Author:  Professor Ispour and Professor Xu												*

; Date: 07-16-2016														*

;************************************************************************

#include <GENERAL.H>

TEMPA	EQU		0X13

TEMPB	EQU		0X14

__CONFIG  0X3FF2

ORG		0X0000

GOTO	START

ORG		0X0004

RETFIE

START

BSF		STATUS,RP0	;Shift to bank 01 to change TRIS registers

MOVLW	0X00

MOVWF	TRISA		;Set RA0,RA1,RA2,RA3 as outputs

MOVLW 	0x07

MOVWF	TRISB		;Set upper five bits of PORTB as outputs

BCF		STATUS,RP0	;Shift to bank 00 for normal operation

LIGHT_LOOP

CLRF	TEMPA

CLRF	TEMPB

BTFSC	PORTB,0		;Check Switch 1

CALL	SWITCH1		;Call switch1 subroutine if switch is on

BTFSC	PORTB,1		;Check Switch 2

CALL	SWITCH2		;Call switch1 subroutine if switch is on

BTFSC	PORTB,2		;Check Switch 3

CALL	SWITCH3		;Call switch1 subroutine if switch is on

MOVF	TEMPA,W		;Move the TEMPA and TEMPB registers that

MOVWF	PORTA		; were constructed depending on swtich positions

MOVF	TEMPB,W		; to the PORTA and PORTB registers to display

MOVWF	PORTB		; on the LEDs

GOTO	LIGHT_LOOP	;Return to top of loop

SWITCH1

; Turns on LED 1 and 4

MOVLW	0X09		;0000 1001 on PORTA

IORWF	TEMPA,F

RETURN

SWITCH2

; Turns on LED 3, 5, 7 and 8

MOVLW	0X04		;0100 on PORTA

IORWF	TEMPA,F

MOVLW	0XD0		;1101 on PORTB

IORWF	TEMPB,F

RETURN

SWITCH3

; Turns on LED 2 and 6

MOVLW	0XFF		;1111 on both Ports

IORWF	TEMPA,F

IORWF	TEMPB,F

RETURN

END

p2. Simulated in Proteus 8:

FIG 6.

Lab4   LCD Display

Objectives

1.  To get familiar with table lookup.

2. To know what is the Liquid Crystal Display (LCD), and how to interface it to the microcontroller in Proteus simulation.

Procedures

p1. create MPLAB project named: demo_4_LCD.

FIG 7.

demo_4_LCD.asm

;***************************************************************************************

;Filename:  IITG Demo 4 LCD Display															   *

;Function:  Demonstrates parallel communications with 2*16 LCD module.

;Modified by  Professor Ispour and Professor Xu														   *

;Date:  07/23/2016																	   *

;***************************************************************************************

#include <General.H>

DELAY1		EQU	0X10		;Delay loop variable

DELAY2		EQU	0X11		;Delay loop variable

DELAY3		EQU	0X12		;Delay loop variable

MSGCOUNT	EQU	0X13		;Message counter variable

TMP			EQU	0x14		;Holds the table offset for the long table

__CONFIG	0X3FF2	;This is the control bits for CONFIG register

ORG		0X0000		;RESET or WDT reset vector

GOTO	START

ORG		0X0004		;Regular INT vector

RETFIE

LCDINIT

BCF		PORTA,1		;RA1=RS, Set RS line Lo for commands

MOVLW	0X30		;Sends reset command to LCD (3 times)

MOVWF	PORTB

CALL	LCDCOMMS

MOVLW	0X30

MOVWF	PORTB

CALL	LCDCOMMS

MOVLW	0X30

MOVWF	PORTB

CALL	LCDCOMMS

MOVLW	0X38		;Sets LCD to advance automatically with each data byte

MOVWF	PORTB

CALL	LCDCOMMS

MOVLW	0X0C

MOVWF	PORTB

CALL	LCDCOMMS

MOVLW	0X01

MOVWF	PORTB

CALL	LCDCOMMS

MOVLW	0X06

MOVWF	PORTB

CALL	LCDCOMMS

MOVLW	0X02

MOVWF	PORTB

CALL	LCDCOMMS

BSF		PORTA,1		;RA1=RS, Set RS line Hi for data

RETURN

LCDCOMMS

BCF		PORTA,0		;RA0=E, set E Lo

NOP

NOP					;3 Instruction cycle delay for LCD to recognize 'E' line being low

NOP

BSF		PORTA,0		;RA0=E, Set Hi

CALL	LCDDELAY

RETURN

LCDDELAY

; 20 mS time delay used for the LCD Module to update after presenting a byte

MOVLW	0X10

MOVWF	DELAY1

LOOP1

MOVLW	0X10

MOVWF	DELAY2

LOOP2

MOVLW	0XF0

MOVWF	DELAY3

LOOP3

DECFSZ	DELAY3,F

GOTO	LOOP3

DECFSZ	DELAY2,F

GOTO	LOOP2

DECFSZ	DELAY1,F

GOTO	LOOP1

RETURN

START

BSF		STATUS,RP0

MOVLW	0XFC		;Set RA0 & RA1 as outputs

MOVWF	TRISA

MOVLW	0X00		;Set all of PORTB as outputs

MOVWF	TRISB

BCF		STATUS,RP0

BSF		PORTA,0

BSF		PORTA,1

CALL	LCDINIT		;Initializing LCD

CLRF	MSGCOUNT	;Sets message counter to 0x00

DISPLAY

MOVF	MSGCOUNT,W	;Put message counter in W

MOVWF	TMP			; tore offset

INCF	MSGCOUNT,F	; ncrement message counter

CALL	SHORT_TABLE	;Call table routinue

MOVWF	PORTB 		;Place ASCII code on LCD Module Inputs

ADDLW	0X00

BTFSC	STATUS,Z	;Check to see if last byte was 0x00

GOTO	STOP		; f so, STOP

CALL	LCDCOMMS	;If not, send byte to LCD

GOTO	DISPLAY		; and retrieve next byte

STOP

GOTO	STOP

SHORT_TABLE

MOVF	TMP,W

ADDWF	PCL,F		;Go to the appropriate RETLW

MSG

DT		"IITG Demo 4"

RETLW	0X00

END

p2. Simulated in Proteus 8:

FIG 8.

IMPORTANT:  Use 2*16 LCD module.

Project Future Works

In future, we can develop other simulation models for Open SUNY such as:

1. logic function design:

2.  Keypad and LCD combined applications:

Also, we can design application for software and hardware co-simulation.